## Slide 1: 5. Audio coding standards
Xavier Serra

## Slide 2: Index
MIDI format
Mono, Stereo and Surround Sound formats
MPEG audio standards
MPEG-1 Layer 3 (MP3)
MPEG-2 Advanced Audio Coding (AAC)
MPEG-4
Dolby Digital (AC3)
Lossless audio coding (FLAC)
FFmpeg

## Slide 3: MIDI

## Slide 4: Mono, Stereo, Surround

## Slide 5: MPEG audio standards
MPEG is the acronym for Moving Pictures Experts Group.
MPEG standardizes the type of information that an encoder has to produce as well as the way in which the decoder has to decompress the information.

## Slide 7: MPEG-1 Audio
Lossy compression of mono and stereo signals.
Sampling frequency: 32KHz, 44.1 KHz, 48 KHz.
Precision 16 bits.
3 compression layers: Layer 1, Layer 2, Layer 3.
  Layer 1: 32-448 kbps, target 192 kbps
  Layer 2: 32-384 kbps, target 128 kbps
  Layer 3: 32-320 kbps, target 64 kbps
Layer 3 is called MP3 format.
  Popular for Internet applications

## Slide 8: MP3 encoder

## Slide 9
Filter bank: Hybrid filter bank. Polyphase filterbank (as used in Layer-1 and Layer2) followed by a Modified Discrete Cosine Transform (MDCT).
Perceptual model to identify masking thresholds based on critical bands of human hearing and using the FFT.
Quantization and coding: Two nested iteration loops. Use of Huffman coding.

## Slide 10: MP3 audio format

## Slide 11: MPEG-2 Advanced Audio Coding (AAC)
Supports up to 5.1 channels.
AAC follows the same basic coding paradigm as Layer-3 (high frequency resolution filterbank, non-uniform quantization, Huffman coding, iteration loop structure using analysis-by-synthesis), but improves on Layer-3 in a lot of details and uses new coding tools for improved quality at low bitrates.
  Higher frequency resolution (1024 frequency lines)
  Improved joint stereo coding
  Improved Huffman coding
  Enhanced block switching
  …

## Slide 12: AAC encoding

## Slide 13
Temporal noise shaping (TNS) tool helps to control temporal shape of quantization noise.
Intensity coding and the coupling reduces perceptually irrelevant information by combining multiple channels in high-frequency regions into a single channel.
Prediction tool further removes redundancies between adjacent frames.
M/S coding removes stereo redundancy based on coding the sum and difference signal instead of the left and right channels.

## Slide 14: MPEG-4 Audio
Extensive scalability and object-based representations.
Variety of applications.
  General audio signals
  Speech signals
  Synthetic audio
  Synthesized speech (structured audio)
More sample frequencies (8-96 kHz).
Arbitrary bit rates and variable frame length.
Higher efficiency and simpler filterbank.
  Uses pure MDCT (modified discrete cosine transform)
  Used in Windows Media Audio

## Slide 16: MPEG-4 integrated tools

## Slide 17: MPEG-4 General Audio coder
Built around MPEG-2 AAC.
Extended features and coder configurations given by the perceptual noise substitution (PNS), long term predictions (LTP), Twin VQ coding, and scalability.

## Slide 18: MPEG-4 Twin VQ in GA coder
Transform-domain Weighted Interleave Vector Quantization.
Vector quantization of the transformed spectral coefficients.
Low bit rates (6-8kb/s).

## Slide 19: MPEG-4 Scalable audio coding
Variable rate enconding/decoding depending on transmission channel capacity.
Decoding at low bit rates (16, 32, or 64 kb/s within high-rate code (64 kb/s).

## Slide 20: MPEG-4 Speech Coding
Bit rates between 2 kb/s and 24 kb/s.
Based on harmonic vector excitation coding (HVXC) and code excited predictive coding (CELP).

## Slide 21: MPEG-4 Structured Audio Coding
Ability to represent and encode efficiently synthetic audio and multimedia content.
Based on the synthesizer-description language called Csound.
Defines a set of syntax and semantic rules corresponding to the Structured Audio orchestra Language (SAOL).

## Slide 22: Dolby AC-3 (Dolby Digital)
De facto standard in most movie houses and home theaters.
Sample rates: 32, 44.1, and 48 kHz
Bit rates: 32–640 kb/s, variable
High-quality output at 64 kb/s per channel
Delay roughly 100 ms
MCDT filter bank
Multiple channels processed as an ensemble
Robust decoder downmix functionality from 5.1 to fewer channels

## Slide 23: Dolby Digital encoder

## Slide 24: Lossless audio coding (FLAC)
High-quality audio without any artifacts.
Compression ratios of 2:1 – 4:1.
Similar to how Zip works, except with FLAC you will get much better compression because it is designed specifically for audio.
Non-proprietary and has an open-source reference implementation.

## Slide 25
Lossless: The encoding of audio (PCM) data incurs no loss of information, and the decoded audio is bit-for-bit identical to what went into the encoder.
Fast: FLAC is asymmetric in favor of decode speed. Decoding requires only integer arithmetic, and is much less compute-intensive than for most perceptual codecs.
Hardware support: FLAC is supported by dozens of consumer electronic devices, from portable players, to home stereo equipment, to car stereo.
Flexible metadata: FLAC's metadata system supports tags, cover art, seek tables, and cue sheets. Applications can write their own APPLICATION metadata once they register an ID.
Seekable: FLAC supports fast sample-accurate seeking. Not only is this useful for playback, it makes FLAC files suitable for use in editing applications.
Streamable: Each FLAC frame contains enough data to decode that frame.

## Slide 26: FFmpeg
A free and open-source software project consisting of a suite of libraries and programs for handling video, audio, and other multimedia files and streams. At its core is the command-line ffmpeg tool itself, designed for processing video and audio files. It is widely used for format transcoding, basic editing (trimming and concatenation), video scaling, video post-production effects, and standards compliance (SMPTE, ITU).

## Slide 27: References
“Chapter 10: Audio coding standards and algorithms” in Andreas Spanias, Ted Painter, and Venkatraman Atti (2007). Audio Signal Processing and Coding. John Wiley & Sons, Inc.
Free lossless audio codec: https://xiph.org/flac/
FFmpeg: https://www.ffmpeg.org/